2005 was an average year for air pollution throughout the UK

Nitrogen Dioxide peaked on the 20th December, at 154 ug/m3 as a peak hour at Bitterne. There was no exceedance of the Nitrogen Dioxide annual mean or hourly mean at any of the automatic monitoring stations in Southampton in 2005, except for Onslow Road, but data was only available for 6 months. PM10 (fine dust) peaked at 63.6 ug/m3, at Redbridge, as a daily mean on the 7th October. Redbridge recorded 9 days of PM10 exceedance this year, Bitterne 3 days and Six Dials  3 days.  The Redbridge Station is close to Redbridge Road which has the highest overall traffic flow and highest number of HGVs.

For more detailed information on the Government's Air Pollution Standards and Banding please see http://laburnum.aeat.co.uk/archive/standards.php

| Pollutant | Redbridge School | BitterneRoad/ Bullar Road by Mays Carpets | Six Dials Junction (provisional data, may be subject to further quality control) |
| --- | --- | --- | --- |
| Particulate (PM10) ug/m3 | Average of 27.2ug/m3, peak day of 63.6ug/m3 on the 7th October 9 days above the daily mean standard Data Capture 93.8% | Average of 23.7 ug/m3, peak day of 59 ug/m3 on the 7th October, 3 days above the standard Data Capture 76% | Average of 26 ug/m3, Peak day of 61 ug/m3 3 days above the standard. Data Capture 91% |
| Nitrogen Dioxide ppb | Average of 36.5 ug/m3 peak hour of 153 ug/m3 on 30th August Data Capture 93.2% | Average of 37 ug/m3, peak hour 154 ug/m3 on 20th December Data Capture 85.6% | Average of 31 ug/m3 peak hour of 113 ug/m3 Data Capture 87% |
| Sulphur Dioxide ppb | Average of 8.5 ug/m3 peak 15 minute of 165ug/m3 on 13th July Data Capture 93.1% | Average of 4.3 ug/m3, peak 15 minute 162 ug/m3 22nd June Data Capture 85.7% | Average of 4 ug/m3 peak 15 minute of 247 ug/m3 Data Capture 90% |
| Carbon Monoxide ppm | N/A | N/A | Average of 0.3 mg m3 peak 8 hour mean of 3.4 mg m3 Data Capture 88.5% |
| Ozone ppb | Average of 30.8 ug/m3 Peak 8 Hour of 102ug/m2 on 28th June 1 day above the standard Data Capture 93.8% | N/A | Average of 33 ug/m3 peak 8 hour mean of 90 ug/m3 0 day above the standard Data Capture 91.3% |
| Benzene | N/A | N/A | 1.69 ug/m3 100% data capture (pumped diffusion tube) |

(ug/m3 = micrograms per cubic metre, ppb = parts per billion, N/A= Non applicable ppm = parts per million)

## Onslow Road, Bevois Valley Oxides of Nitrogen Station

In 2005 a small roadside monitoring station was installed opposite 3 Onslow Road on the pavement. This is within the Air Quality Management Area. After some initial problems with interruptions to the power supply, data was gathered from 15/7/05- 31/12/05 with 98% data capture. The Nitrogen Dioxide mean for this 6 month period was

48.7 ug/m3, in line with the modelling prediction for this location. O.S. Grid Ref: 442304, 112771

## Description of the Monitoring Stations in Southampton

DEFRA Automatic Urban Network Station, Brintons Road, by Six Dials Junction, established 1994, classified as an Urban Centre site. Approx. 8metres from the kerb of Northam Road, approx. 38000 vehicles per day. Monitors NOx, SO2, O3, CO, PM10. and benzene by pumped diffusion tube.  A residential area with houses close to the road.

O.S. Grid Ref: 442583, 112248.

Mobile Unit, (Groundhog) currently sited at Bitterne Road opposite Mays Carpets. Monitors NO2, SO2, and PM10. Residential Area approx. 10 metres from Bitterne Road/Bullar Road Traffic Lights and close to railway line.

Previously sited at the Civic Centre Front Car Park & Wimpson Lane, Millbrook. 35,000 vehicles per day, 2.3% HGV, 30mph speed limit. On the edge of the Air Quailty Management Area. O.S. Grid Ref: 443987, 113340

Permanent Station, at Redbridge Community School, established April 99. Approx. 8 metres from the kerb of Redbridge Road the most heavily trafficked road in Southampton, a 3-lane dual carriageway, and 50-mph speed limit. This road is the designated route into the port for HGVs, approx. 80,000 vehicles per day, 7% HGV. Monitors NO2, SO2, O3 and PM10. A residential area with several schools and sports grounds next to the road.

O.S. Grid Ref: 437549, 113721.

Roadside Station, opposite 3 Onslow Road, within the Bevois Valley Air Quality Management Area. Established in July 2005. 18,000 vehicles per day, 2.6% HGV, 30mph speed limit. Only monitors oxides of nitrogen. 2 metres from the kerb. O.S. Grid Ref: 442304, 112771.

| Pollutant | Air Quality Objective | Date to be achieved by |
| --- | --- | --- |
|  | Concentration | Measured as |  |
| Particles (PM10) | 50 ug/m3 (gravimetric) not to be exceeded more than 35 times a year (TEOM data multiply by 1.3) | Daily (24 hour mean) | 31.12.2004 |
| Nitrogen Dioxide | 105 ppb (200 ug/m3) not to be exceeded more than 18 times a year | 1 hour mean | 31.12.2005 |
|  | 21 ppb (40 ug/m3) | annual mean | 31.12.2005 |
| Sulphur Dioxide | 132 ppb (350 ug/m3) not to be exceeded more than 24 times a year | 1 hour mean | 31.12.2004 |
|  | 47 ppb (125 ug/m3) not to be exceeded more than 3 times a year | 24 hour mean | 31.12.2004 |
|  | 100 ppb (266 ug/m3) not to be exceeded more than 35 times a year | 15 minute mean | 31.12.2005 |
| Carbon monoxide | 10ppm (11.6 mg/m3) | running 8-hour mean | 31.12.2003 |
| Benzene | 5.00 ug/m3 | annual mean | 31.12.2010 |
| 1,3 Butadiene | 1ppb (2.25 ug/m3) | running annual mean | 31.12.2003 |
| Lead | 0.5 ug/m3 | annual mean | 31.12.2004 |
|  | 0.25ug/m3 | annual mean | 31.12.2008 |
| Ozone | 50 ppb (100ug/m3) not to be exceeded more than 10 times a year | Daily maximum of running 8 hour mean | 31.12.2005 |

# Text boxes

SOUTHAMPTON CITY AIR QUALITY

REPORT FOR 2005

Any queries about air quality please contact:

Environmental Health Service (Pollution & Safety), Southbrook Rise, 4-8 Millbrook Road East,

Southampton, SO15 1YG.  Telephone 023 8083 2170

Issued by: ENVIRONMENTAL SERVICES AND CONSUMER PROTECTION DIVISION

Printed and published by Southampton City council.

National Air Quality Standards

The table below summarises the National Air Quality Standards which are set out in the National Air Quality Strategy.  Southampton City Council has a statutory duty to achieve these standards by the assigned date.