2007 recorded similar levels of air pollution to 2006.

Particulate dust (PM10) peaked at all 3 monitoring stations on the 25th March, 104 ug/m3 ,this was part of a southern england dust episode linked to Saharan sandstorms.

Nitrogen Dioxide peaked on the 7th February, at 176 ug/m3 as a peak hour at Bitterne and 203.6 ug/m3 at Onslow Road on the 11th December. The Onslow Road peak hour was just above the national hour standard,

only one exceedance was recorded of this standard.  Both Redbridge and Bitterne recorded nitrogen dioxide

levels just below the 40 ug/m3 annual mean, bitterne by only a margin of 0.3 ug/m3.

Onslow Road  recorded  the highest nitrogen dioxide annual mean at 56.0 ug/m3, well above the standard.

This station is within the Bevois Valley Air Quality Management Area. There are residential flats above the

shops at this location, a similar distance to the kerb as the monitoring station.

This location is representative of residents exposure.

Redbridge recorded 11 days of PM10 exceedance this year, Bitterne 7 days and Six Dials 13 days.  The Redbridge School Station had the highest annual mean for PM10 .This is unsurprising as it is only 8m from Redbridge Road which has the highest overall traffic flow and highest number of HGVs in the City.

For more detailed information on the Government's Air Pollution Standards and Banding please see http://laburnum.aeat.co.uk/archive/standards.php

| Pollutant | Redbridge School | BitterneRoad/ Bullar Road by Mays Carpets | Six Dials Junction |
| --- | --- | --- | --- |
| Particulate (PM10) ug/m3 | Average of 29.5ug/m3, peak day of 104ug/m3 on the 25th March 11 days above the daily mean standard Data Capture 94% | Average of 25.6 ug/m3, peak day of 102 ug/m3 on the 25th March, 7 days above the standard Data Capture 91.3% | Average of 23 ug/m3, Peak day of102 ug/m3 On 25th March 13 days above the standard. Data Capture 98.3% |
| Nitrogen Dioxide ug/m3 | Average of 39.0 ug/m3 peak hour of 159 ug/m3 on 16th November Data Capture 94% | Average of 39.7 ug/m3, peak hour 176 ug/m3 on 7th February Data Capture 88% | Average of 34 ug/m3 peak hour of 160 ug/m3 Data Capture 77.6% |
| Sulphur Dioxide ug/m3 | Average of 8.8 ug/m3 peak 15 minute of 122ug/m3 on 21st April Data Capture 86% | Average of 2.4 ug/m3, peak 15 minute 114 ug/m3 on the 31st May Data Capture 89.5% | Average of 3 ug/m3 peak 15 minute of 82 ug/m3 Data Capture 98.1% |
| Carbon Monoxide ug/m3 | N/A | N/A | Average of 0.2 mg m3 peak 8 hour mean of 2.2 mg/ m3 Data Capture 96.9% |
| Ozone ug/m3 | Average of 37 ug/m3 Peak 8 Hour of 111ug/m2 on 2nd April 2 days above the standard Data Capture 94% | N/A | Average of 31 ug/m3 peak 8 hour mean of 91 ug/m3 0 days above the standard Data Capture 97.3% |
| Benzene ug/m3 | N/A | N/A | Average of 1.0 ug/m3 100% data capture (pumped diffusion tube) |

(ug/m3 = micrograms per cubic metre, ppb = parts per billion, N/A= Non applicable ppm = parts per million)

## Onslow Road, Bevois Valley Oxides of Nitrogen Station

In 2005 a small roadside monitoring station was installed opposite 3 Onslow Road on the pavement. This is within the Air Quality Management Area. The Nitrogen Dioxide mean for 2007 was 56.0 ug/m3.

The highest monitored level in Southampton. Peak hour was 203.6 ug/m3 on the 11th December.   Data Capture was 90.6%  O.S. Grid Ref: 442304, 112771.

Millbrook Road junction of Waterhouse Lane Oxides of Nitrogen Station

In September 2007 a small roadside monitoring station was installed at the junction with Waterhouse Lane.

This is within the new Millbrook Road Air Quality Management Area. The Monitoring Site is funded by Marchwood Power Station who are required to monitor the impact of the new 850 MW gas fired power station just across Southampton Water next to the existing Incinerator. This new site is downwind of the power station.

The power station is due to commence operation december this year.

Ratified data for the period 20/9/2007 - 14/5/2008 with good 97% data capture produced a mean over this period of 54.6 ug/m3 for Nitrogen Dioxide, well above the annual mean standard. The peak hour was 202 ug/m3 .

This initial data validates  the accuracy of the existing diffusion tubes already located here and confirms the decision to declare an Air Quality Management Area along the road where there are residential properties close to the kerb.

## Description of the Monitoring Stations in Southampton

DEFRA Automatic Urban Network Station, Brintons Road, by Six Dials Junction, established 1994, classified as an Urban Centre site. Approx. 8metres from the kerb of Northam Road, approx. 33,000 vehicles per day, 3.5% HGV. Monitors NOx, SO2, O3, CO, PM10. and benzene by pumped diffusion tube.  A residential area with houses close to the road.  O.S. Grid Ref: 442583, 112248.

Mobile Unit, Bitterne Road in railway station car park. Monitors NO2, SO2, and PM10.

Residential Area approx. 10 metres from Bitterne Road/Bullar Road Traffic Lights and close to railway line.

33,000 vehicles per day, 3.5% HGV, 30mph speed limit. On the edge of the Air Quailty Management Area. O.S. Grid Ref: 443987, 113340

Redbridge Community School, established April 99. Approx. 8 metres from the kerb of Redbridge Road the most heavily trafficked road in Southampton, a 3-lane dual carriageway, and 50-mph speed limit. This road is the designated route into the port for HGVs.  Average Daily Traffic count of 76,000 vehicles per day, 8% HGV. Monitors NO2, SO2, O3 and PM10. A residential area with several schools and sports grounds next to the road.

O.S. Grid Ref: 437549, 113721.

Opposite 3 Onslow Road, within the Bevois Valley Air Quality Management Area. Established in July 2005. 18,000 vehicles per day, 2.6% HGV, 30mph speed limit. Only monitors oxides of nitrogen. 2 metres from the kerb. O.S. Grid Ref: 442304, 112771.

Junction of Millbrook Road/Waterhouse Lane, Freemantle. Within the Millbrook Road AQMA, established September 2007. Funded by Marchwood Power Station as part of a planning condition to monitor downwind of the stack.  Monitors oxides of nitrogen and ozone. 6m from the kerb, 53,000 vehicles per day, 4.5% HGV, 50mph speed limit. Grid Reference: 439702,112768

| Pollutant | Air Quality Objective | Date to be achieved by |
| --- | --- | --- |
|  | Concentration | Measured as |  |
| Particles (PM10) | 50 ug/m3 (gravimetric) not to be exceeded more than 35 times a year (TEOM data multiply by 1.3) | Daily (24 hour mean) | 31.12.2004 |
| Nitrogen Dioxide | 105 ppb (200 ug/m3) not to be exceeded more than 18 times a year | 1 hour mean | 31.12.2005 |
|  | 21 ppb (40 ug/m3) | annual mean | 31.12.2005 |
| Sulphur Dioxide | 132 ppb (350 ug/m3) not to be exceeded more than 24 times a year | 1 hour mean | 31.12.2004 |
|  | 47 ppb (125 ug/m3) not to be exceeded more than 3 times a year | 24 hour mean | 31.12.2004 |
|  | 100 ppb (266 ug/m3) not to be exceeded more than 35 times a year | 15 minute mean | 31.12.2005 |
| Carbon monoxide | 10ppm (11.6 mg/m3) | running 8-hour mean | 31.12.2003 |
| Benzene | 5.00 ug/m3 | annual mean | 31.12.2010 |
| 1,3 Butadiene | 1ppb (2.25 ug/m3) | running annual mean | 31.12.2003 |
| Lead | 0.5 ug/m3 | annual mean | 31.12.2004 |
|  | 0.25ug/m3 | annual mean | 31.12.2008 |
| Ozone | 50 ppb (100ug/m3) not to be exceeded more than 10 times a year | Daily maximum of running 8 hour mean | 31.12.2005 |

# Text boxes

SOUTHAMPTON CITY AIR QUALITY

REPORT FOR 2007

Any queries about air quality please contact:

Environmental Health Service (Pollution & Safety), Southbrook Rise, 4-8 Millbrook Road East,

Southampton, SO15 1YG.  Telephone 023 8083 2170

Issued by: ENVIRONMENTAL SERVICES AND CONSUMER PROTECTION DIVISION

Printed and published by Southampton City council.

National Air Quality Standards

The table below summarises the National Air Quality Standards which are set out in the National Air Quality Strategy.  Southampton City Council has a statutory duty to achieve these standards by the assigned date.